Evaluating material models in TensorMechanics, re: finite strain, and comparing to SolidMechanics, both in 2D and 3D

Problem setup:
Mesh: generated mesh, 1x1 in 2D (1x1x1 in 3D)
Coordinate system: xy(z)
AuxVariables: strain_yy, stress_yy (TM = RankTwoAux; SM = MaterialTensorAux)
BCs: FunctionPresetBC, disp_y = -0.2*t on top, sides (+ back/front) constrained
Time: end_t = 4.0

in SM: Material = Elastic, NonlinearPlaneStrain

in TM: Material = ComputeIsotropicElasticityTensor, ComputePlaneStrain (ComputeFiniteStrain in 3D), ConputeFiniteStrainElasticStress

Theory:

The disp_y at the end of four seconds should be -0.8. This is correct in all four simulations. Based on this displacement, the final strain_yy should be:

Results:

– Requires small time step: default dt = 1.0, strain_yy (and therefore stress_yy) results very incorrect:

Where material definitions are:

– With small time step, strain results are correct (dt = 0.01):

These strain values are very close to the expected value based on theory (-1.6094379124341).

Conclusions:

– Model is accurate for strain with small time step (dt=0.1), in both SM and TM.
– Model is very inaccurate for strain with larger time step (dt=1.0), in both SM and TM.
– To resolve time step issue, model used to evaluate strain would need to be changed (currently Rashid, 1993).
– Using dt=0.1 also yields relatively accurate results (-1.6023377300219 for strain_yy in 2D TM).